## Slide 1: Dilated Dense-Unet for Esophageal Gross Tumor volume Segmentation in CT images
(3D Convolutional Neural Networks)
LKEB
Leiden
Sahar Yousefi
Notes: Thank you for coming to my presentation

## Slide 2: Problem & Challenges
The problem definition and challenges

## Slide 3: Problem definition
Designing a Convolutional neural network for automating the process of esophageal GTV segmentation in CT images
GTV in Ground truth
Output of the method
CNN

## Slide 4: Manual delineation challenge
without delineation
with delineation
Low contrast of tumor
Notes: Here the left figure shows the ct scan of one patient with esophageal cancer without delineation and the right figure shows the delineated tumor in that scan
If one looks at the left image, it is really hard to say when the tumor starts and when it stops

## Slide 5: Manual delineation challenges
For manual delineation of tumor in CTs Physicians use additional knowledge:
      A combination of clinical history
      Endoscopy findings
      Other imaging modalities (PET)
    Obtaining this data is hard, time consuming and expensive! 
    Still is an ill-posed problem!! 
Notes: Developing an automatic and reliable approach for esophageal GTV segmentation is desirable

## Slide 6: Manual delineation still is an ill-posed problem!
Goal: assessing delineation variability of the GTV between CT and combined PET-CT in esophageal cancer patients in a multi-institutional study
PET significantly influenced the delineated volume in some cases, however its impact on observer variation was limited
Phase 1- The GTV of the primary tumour was delineated by 20 observers on CT, with available clinical and diagnostic information
Phase 2- After fusion of the FDG-PET scan, the GTV was
adjusted based on the visual interpretation of the FDG-PET scan

## Slide 7: OUR Previous work
Flash back

## Slide 8: Problem of the traditional CNN connectivity
Typical CNN layers
Issue: information can wash out by the time it reaches the end of the network!
Solution: Loop connectivity pattern
Conv
Conv
Conv
…
Conv
Conv
Conv
Notes: Issue: As information passes through many layers, it can vanish and wash out by the time it reaches the end /or beginning of the network!

## Slide 9
Advantages:
    Improve the flow of information and gradients throughout the network
    Leads to feature re-usability
+
+
+
+
+

## Slide 10
Advantages:
    Improve the flow of information and gradients throughout the network
    Leads to feature re-usability
+
+
+
+
+
Dense Block (DB)

## Slide 11: Our previous work
Yousefi, Sahar, et al. "Esophageal Gross Tumor Volume Segmentation Using a 3D Convolutional Neural Network." MICCAI 2018.

## Slide 12: Dataset- the MICCAI paper
Dataset 1: contains 21 distinct patients
    For each patient: five repeat CT scans captured at different time points.
    For three time points, there was one 3D CT scan,
    For two time points there were one 3D CT scan and one 4D CT scan (consisting of 10 breathing phases)
Dataset 2: contains 29 distinct patients
    A single 3D CT scan per each patient
Delineation:
    For each scan there was a corresponding esophageal GTV segmentation
    Dataset 1: done by one physician
    Dataset 2: done by multiple physician!
  Scanning protocol and scanners:
    Same for the both dataset

## Slide 13: Results
Eight (8/85) scans had a DSC<0.50
Mostly caused by the presence of air cavities and foreign bodies (feeding tubes, surgical clips) in the GTV
Were rarely seen in the training data

## Slide 14
Current work

## Slide 15: Contributions
  Data:
    Enriched the 2nd dataset with 120 scans from 120 distinct patients
Network structure
    Leveraged dilated convolutional layers in Dense blocks
      Increasing the receptive field
      Managing GPU memory

## Slide 16: Dataset- present work
Dataset 1: contains 21 distinct patients
    For each patient: five repeat CT scans captured at different time points.
    For three time points, there was one 3D CT scan,
    For two time points there were one 3D CT scan and one 4D CT scan (consisting of 10 breathing phases)
Dataset 2: contains 106 distinct patients
    A single 3D CT scan per each patient
Delineation:
    For each scan there was a corresponding esophageal GTV segmentation
    Dataset 1: done by one physician
    Dataset 2: done by multiple physician!
  Scanning protocol and scanners:
    Same for the both dataset

## Slide 17: Receptive field
The region in the input space that a particular CNN’s feature is effected by
Receptive field: 3*3
Receptive field: 5*5
CNN
Conv
CNN
Conv
Conv
input

## Slide 18: Dilated convolutional layer
Exponential expansion of the receptive field
Standard Convolution
Dilated Convolution
Receptive field of a Conv layer:
Receptive field of a max-pool layer:
k=kernel size
p=padding
s=stride
d=dilation

## Slide 19: Proposed architecture
Receptive field increased:
from 43*43*43 (in MICCAI work) to 61*61*61

## Slide 20: Training and testing details
The network is trained patch based
    Manages the GPU memory limitation
    Increases data
    Reduces overfitting
Multithreading has been used for extracting the patches
    Patch extraction is done in parallel with training the network
      While the GPU is busy with training the network by the current patches, the next patches are extracted to be ready for the next feeding
Data augmentation
    Adding noise randomly to the patches
  Managing the data imbalance problem (ratio of tumor vs background is low)
    Patches mostly are extracted from tumor region (75%)

## Slide 21: Training and testing details
  Data has been splitted in
    Training set
    Validation set
    Test set
For evaluation the network 4-fold cross validation has been used
Experimental results have been done in three steps
    Experiment #1: using the both datasets for training
    Experiment #2: using only the second dataset for training
    Experiment #3: using only the first dataset for training

## Slide 22: Experimental results
Experimental results

## Slide 23: DSC value for one fold of the 1st experimental trial
Chart: DSC
6 patients from the 1st dataset
25 patients from the 2nd dataset

## Slide 24: Mean surface distance for one fold of the 1st experimental trial
Chart: MSD
6 patients from the 1st dataset
25 patients from the 2nd dataset

## Slide 25: Comparison between the result of the 1st dataset and the 2nd dataset
DSC-SC: results of the output of the network
DSC+SC: selecting the component which has an overlay with the ground truth manually

## Slide 26: Results- 4 different folds (the 1st experimental trial: Training on the both datasets)
Chart: DCS
Chart: 
Chart: 
Chart: 
Dataset #1
Dataset #2

## Slide 27: Results- 4 different folds (the 2nd experimental trial: training only on the second dataset)
Chart: DSC
| TEST086_2016-12-21 | TEST087_2017-02-16 | TEST088_2017-02-20 | TEST089_2017-02-14 | TEST090_2017-02-27 | TEST091_2017-03-13 | TEST092_2017-04-18 | TEST093_2017-04-20 | TEST094_2017-04-25 | TEST095_2017-04-19 | TEST096_2017-05-09 | TEST097_2017-05-24 | TEST098_2017-07-11 | TEST099_2017-07-27 | TEST100_2017-08-02 | TEST101_2017-08-03 | TEST102_2017-08-15 | TEST103_2018-01-11 | TEST104_2017-09-04 | TEST105_2018-03-26 | TEST106_2018-01-10 | TEST107_2017-10-09 | TEST108_2017-09-18 | TEST109_2017-11-16 | TEST110_2017-11-13
 | 0 | 0.34 | 0.64 | 0.56 | 0.65 | 0.4 | 0.74 | 0.45 | 0.26 | 0.49 | 0.28 | 0 | 0.79 | 0.6 | 0.26 | 0.44 | 0.04 | 0.27 | 0.87 | 0.76 | 0 | 0.09 | 0.49 | 0 | 0.22
Chart: 
| TEST086_2016-12-21 | TEST087_2017-02-16 | TEST088_2017-02-20 | TEST089_2017-02-14 | TEST090_2017-02-27 | TEST091_2017-03-13 | TEST092_2017-04-18 | TEST093_2017-04-20 | TEST094_2017-04-25 | TEST095_2017-04-19 | TEST096_2017-05-09 | TEST097_2017-05-24 | TEST098_2017-07-11 | TEST099_2017-07-27 | TEST100_2017-08-02 | TEST101_2017-08-03 | TEST102_2017-08-15 | TEST103_2018-01-11 | TEST104_2017-09-04 | TEST105_2018-03-26 | TEST106_2018-01-10 | TEST107_2017-10-09 | TEST108_2017-09-18 | TEST109_2017-11-16 | TEST110_2017-11-13
 | 0 | 0.35 | 0.65 | 0.55 | 0.7 | 0.6 | 0.76 | 0.59 | 0.28 | 0.27 | 0.32 | 0 | 0.79 | 0.57 | 0.38 | 0.55 | 0.15 | 0.28 | 0.88 | 0.74 | 0 | 0.14 | 0.51 | 0 | 0.35
Chart: 
| TEST086_2016-12-21 | TEST087_2017-02-16 | TEST088_2017-02-20 | TEST089_2017-02-14 | TEST090_2017-02-27 | TEST091_2017-03-13 | TEST092_2017-04-18 | TEST093_2017-04-20 | TEST094_2017-04-25 | TEST095_2017-04-19 | TEST096_2017-05-09 | TEST097_2017-05-24 | TEST098_2017-07-11 | TEST099_2017-07-27 | TEST100_2017-08-02 | TEST101_2017-08-03 | TEST102_2017-08-15 | TEST103_2018-01-11 | TEST104_2017-09-04 | TEST105_2018-03-26 | TEST106_2018-01-10 | TEST107_2017-10-09 | TEST108_2017-09-18 | TEST109_2017-11-16 | TEST110_2017-11-13
 | 0.15 | 0.44 | 0.55 | 0.58 | 0.68 | 0.36 | 0.75 | 0.75 | 0.29 | 0.5 | 0.54 | 0 | 0.79 | 0.62 | 0.51 | 0.48 | 0.08 | 0.3 | 0.87 | 0.7 | 0 | 0.17 | 0.57 | 0 | 0.23
Chart: 
| TEST086_2016-12-21 | TEST087_2017-02-16 | TEST088_2017-02-20 | TEST089_2017-02-14 | TEST090_2017-02-27 | TEST091_2017-03-13 | TEST092_2017-04-18 | TEST093_2017-04-20 | TEST094_2017-04-25 | TEST095_2017-04-19 | TEST096_2017-05-09 | TEST097_2017-05-24 | TEST098_2017-07-11 | TEST099_2017-07-27 | TEST100_2017-08-02 | TEST101_2017-08-03 | TEST102_2017-08-15 | TEST103_2018-01-11 | TEST104_2017-09-04 | TEST105_2018-03-26 | TEST106_2018-01-10 | TEST107_2017-10-09 | TEST108_2017-09-18 | TEST109_2017-11-16 | TEST110_2017-11-13
DCS-LC | 0 | 0.39 | 0.66 | 0.49 | 0.62 | 0.33 | 0.82 | 0.7 | 0.35 | 0.45 | 0.46 | 0 | 0.79 | 0.62 | 0.45 | 0.52 | 0.03 | 0.28 | 0.88 | 0.69 | 0 | 0.04 | 0.51 | 0 | 0.27
Dataset #2

## Slide 28: Results- 4 different folds (the 3rd experimental trial: training only on the first dataset)
Chart: DSC
Chart: 
Chart: 
Chart: 
Dataset #1
Dataset #2

## Slide 29: What is a CNN sensitive to?
Data!
    Diversity of the cases
      It is hard to find a good CNN if the data be too diverse
    Cases which can be seen rarely (a few times) in training can not be segmented successfully in test set
      Different shape of tumor
      Different and rare anatomies
      Diseases or disorders in the patients which is not common in the data
    What we can do?
      Inspection of the data!

## Slide 30: A successful case 1st dataset
0.89 | 0.90
DCS-LC | DCS+LC
Manual delineation
Network result

## Slide 31: A successful case 1st dataset
0.87 | 0.87
DCS-LC | DCS+LC
Manual delineation
Network result

## Slide 32: A patient with some air pockets and a feeding tube
Air pocket
Feeding tube
Manual delineation
Network result

## Slide 33: Not a very good case
0.6 | 0.65
DCS-LC | DCS+LC
Manual delineation
Network result
Notes: Test 99

## Slide 34: Not a good case
0.42 | 0.46
DCS-LC | DCS+LC

## Slide 35: Difficulty raised by using contrast agent
Usually contrast agents are not used for GTV delineation!
we have a couple of scans with contrast agents in the dataset
Esophagus

## Slide 36: A failure case: difficulty raised by contrast agent
0.31 | 0.4
DCS-LC | DCS+LC
Manual delineation
Network result
Notes: Test 026

## Slide 37: Anatomy variations: -Hiatal hernia
The hiatus is an opening in the diaphragm
In a hiatal hernia the stomach bulges up into the chest through hiatus

## Slide 38: A failure case: a patient with hiatal hernia Anatomy variation
Manual delineation
Network result

## Slide 39: Anatomy variations: -Esophagus location variation
In most of the cases esophagus is located in front of spine and left of aorta!
In some patients the esophagus has moved to the right of aorta!
Spine
Aorta
Aorta
Spine
Manual delineation
Network result

## Slide 40: A failure case: a patient with esophagus location variation
0.03 | 0.05
DCS-LC | DCS+LC
Manual delineation
Network result
Notes: Variation of esophagus 5%
Test 033

## Slide 41: Anatomy variations: Part of the lung has been removed!
Esophagus

## Slide 42: A failure case: difficulty raised by a different anatomy
0 | 0
DCS-LC | DCS+LC
Manual delineation
Network result

## Slide 43: Anatomy variations: Absence of fat around the esophagus!
Fat around the esophagus has been lost!
Esophagus

## Slide 44: A failure case: difficulty raised by a different anatomy
0.10 | 0.20
DCS-LC | DCS+LC
Manual delineation
Network result
Notes: test097

## Slide 45: Conclusions
Conclusions

## Slide 46: Conclusion
What we did?
    Enriched the data compared to our previous work
      A bigger dataset with more diversity
    Used dilated layers for increasing the receptive field of the network
  Due to its difficulties, the problem of automating the esophageal GTV segmentation has not been touched too much
    There are only a few literatures in this field
    Data diversity is one of the most challenging issues in this problem
    Enriching the dataset with similar cases can be helpful
    This work shows that using CNN for this purpose is very promising

## Slide 47
Thank you for your attention!